Electric bell

- When there is no electricity, the hammer is in contact with the contact rod.

- When the switch is pressed, the circuit is said to be closed. Electricity flows through the circuit; the electromagnet produces magnetic force and attracts the hammer. The hammer strikes the bell and creates a sound.

- When the hammer strikes the bell, the hammer is no longer in contact with the contact rod which causes a short circuit, thus cutting the flow of electricity.

- Without electricity, the electromagnet loses its magnetic force. The hammer returns to its original position and touches the contact rod again.

- The process is repeated while the switch is pressed and therefore the electric bell keeps on ringing.